## Slide 1: SOLID PROPULSION TEAM REPORT WEEK 10
NAKUJA PROJECT

## Slide 2: WEEK 10 OBJECTIVE
3D printing more new mold castings. #111
Calculation of the masses of components for cooking grains. #130
Cooking grains. #83
Calculation of bolts. #129
Calculations of motor casing thickness. #128
Motor casing boring. #131

## Slide 3: #111 3D PRINTING OF MORE NEW MOLD CASTING TOOLS.

## Slide 4: #130 Calculation of masses of cooking grains components.
Using a grain with 16.98mm diameter port:
Simulated mass of 1 grain= 529g
15% allowance for waste:
Taking ratio of : Sorbitol = 65 : 35
Mass of : 0.65 608.4g = 395.46g.
Mass of solid sorbitol : 0.35 608.4 = 212.94g.
Liquid Sorbitol contains 70% sorbitol.

## Slide 5: Continue
Mass of liquid sorbitol to be measured:
Mass of iron (iii) oxide =1% total mass

## Slide 6: Continue
ELEMENT | MASS (g)
POTASSIUM NITRATE | 395.46
SORBITOL | 304.2
IRON(iii) OXIDE | 6.084
For cooking one grain the following measurements shall be used:

## Slide 7: #83 COOKING GRAINS
Cooked 2 grains using 25mm diameter.
Cooked 2 grains using 16.98mm port diameter

## Slide 10: #128 Calculations of motor casing thickness.
Considering design pressure:
……… (1)
where:
      - Yield strength.
      Design Pressure
      t – thickness
      - Outer diameter
      - Safety factor
From equation (1)
t
For:
        = 8.02 Mpa
        = 73mm
        = 1.87
        = 220MPa
  t
      = 2.488 mm
      t =2.5mm
  Thus = 73mm
  = 68mm
  t = 2.5mm

## Slide 11: Continued
Considering Burst pressure:
For the thickness 2.5mm:
where:
      - Yield strength.
      Burst Pressure
      t – thickness
      - Outer diameter
      B – Burst Factor
For:
        t= 2.5mm
        = 73mm
        B= 1.726
        = 220MPa
      = 26.0082MPa
      =26MPa

## Slide 12
https://www.nakka-rocketry.net/softw.html

## Slide 13: #129 CALCULATION OF BOLTS
The maximum pressure (PMax)as simulated in open motor was 8.02Mpa.
The pressure force (F­­­P):
Inside diameter(d) = 68mm

## Slide 14: Continue
M8 Bolt cross-section area= 50.265mm2
Force acting on each bolt:
F­B=, Where n= number of bolts
Using 8 M8 Bolts:
The shear stress (τ) acting on each bolt
τ =­­
The yield strength of mild steel bolt is 250N/mm2.
Using von misses yield criterion to calculate the maximum shear stress:

## Slide 15: Continue
Using a safety factor of 1.5:
72.431 < 96.67
The design using 8 M8 bolts is safe.

## Slide 16: Comparison of the maximum allowable stress to different bolt sizes for optimum design

## Slide 17: #131 Motor casing boring.
Broken boring tool
Boring of motor casing.

## Slide 18: IGNITION CIRCUIT
Added JST connectors.

## Slide 19: CHALLENGES
Melting of casting tools – Increase the infill to 70%.
Destroyed load cell – Purchase of new load cell
Broken boring tool.
Purchase of new ESPs.

## Slide 20: NEXT WEEK’S OBJECTIVES
Boring of motor casing.
Purchase more ESPs and load cell.
Repair of the motor holder and test stand.
3D printing more casting tool.
Cooking grains.
Making ignitors.

## Slide 21: THANK YOU