## Slide 1: WEEK 4 SOLID TEAM REPORT
NAKUJA PROJECT

## Slide 2: WEEKLY OBJECTIVES
COOKING
COOKING OF GRAINS
TEST STAND
CALCULATIONS AND WELDING
MOTOR HOLDER
MAKING A NEW ALUMINIUM MOTOR HOLDER
DISASSEMBLY AND ANALYSIS
MOTOR DISASSEMBLY AND STATIC TEST RESULTS ANALYSIS
IGNITION CIRCUIT
PREPARATION OF IGNITION CIRCUIT AND IGNITORS
NOZZLE
SIMULATION OF AIR FLOW IN THE NOZZLE

## Slide 3: #40 COOKING OF THE GRAINS
Three grains were cooked and casted

## Slide 4: COOKING OF THE GRAINS
PREVIOUS GRAINS
CURRENT GRAINS

## Slide 5: #55 TESTSTAND CALCULATION
CALCULATION OF THE ANGLELINE BAR SUPPORTING LOADCELL ON THE TESTSTAND

## Slide 6: TESTSTAND CALCULATION
FROM THE CALCULATIONS:
L-Shaped bar can withstand more force and moment than the flat bar(minimum deflection on L-shaped)

## Slide 7: #56 REINFORCEMENT OF TESTSTAND
L-shaped bars used to reinforce the load cell support.

## Slide 8: #57ALUMINIUM MOTOR HOLDER

## Slide 9: #58MOTOR DISASSEMBLY
GOOD CONDITION | DAMAGED
BULKHEAD AND ITS O-RINGS | NOZZLE O-RINGS
NOZZLE | MOTOR HOLDER
MOTOR CASING | 
BOLTS | 

## Slide 10: #46 STATIC TEST RESULTS ANALYSIS
A maximum thrust of 22.031kgf(216N).
Failure of the loadcell support at 216N??
WHY???

## Slide 11: #59 IGNITION CIRCUIT AND IGNITORS

## Slide 12: #44 NOZZLE SIMULATION
BOUNDARY CONDITIONS
Inlet-7.5Mpa gauge
Outlet-101.325KPa(atmospheric)
FINDINGS
The flow of gas at outlet increased to supersonic speed(Mach>1)
The design of the nozzle is okay

## Slide 13: CHALLENGES
An extra longer power extension cable needed.
M4-M8 Drill bits required.

## Slide 14: NEXT WEEK’S OBJECTIVES
Machining of:
      Nozzles
      Bulkheads
Design of the casting tool
Agree on bolting method to airframe
Fabrication of ignition circuit
Cooking of grains
Storage of grains method

## Slide 15: THANK YOU