## Slide 1: WEEK 3 PROGRESS REPORT
AIRFRAME TEAM

## Slide 2: Objectives
Tasks completed
#29 Prefabricated aluminum tube search.
#30 Designing on how to mount the solid rocket motor onto rocket.
#35 Calculating the strength of the fastening bolts.
#41 Designing of a faster assembly mechanism.
#22 Designing of a cone shaped deflector.
Remaining Tasks:
Fabrication

## Slide 3: Prefabricated aluminium tube search
Company | Location | Material present
Hydro aluminium company | Silver business park | AA 6063 tubes and shafts
Aquva agencies | Industrial Area | Currently AA1050 sheet
Kens metal company | Industrial Area | AA7075 Sheet
Suggested area | Kariobangi | Both material AA6061 and fabrication
Material in search- aluminium tube of grade AA 6061 of internal diameter of 75mm and thickness of 2mm.

## Slide 4: METHODOLOGY
STEP 1
Simulation using OpenRocket
STEP 2
Drawing using SolidWorks
STEP 3
Simulation using Ansys and SolidWorks
DESIGN AND SIMULATION

## Slide 5: OPENROCKET SIMULATION
Obtaining the motor casing diameter, the desired design was simulated.

## Slide 6: SOLIDWORKS DRAWINGS
Parts and drawings

## Slide 7: Solidworks simulation
Aerodynamics Simulation of the rocket

## Slide 8: ANSYS SIMULATIONS
Airframe aerodynamics investigations: velocity, and pressure.

## Slide 9: Mounting the solid rocket motor onto rocket
N3 design Proposed design
Ensure an airtight assembly and use of a single bolt cutting through the airframe,motor casing and the nozzle.
4 bolts holding motor casing to the airframe.
4 bolts holding the motor casing to the nozzle and buckle head.

## Slide 10: Calculating the strength of the fastening bolt
Double shear of the bolt.
Estimated total mass=10kg
Equations used:
F.chamber = P. max X Cross S.A
F.airframe(weight) = Mass X Acceleration
Shear stress at each bolt = Total Force /C.S.A
= 124.4 N/mm2, which is < 176 N/mm2

## Slide 11: DESIGN OF A FASTER ASSEMBLY MECHANISM
Challenge faced in N3: misalignment of the holes of the airframe, and the other rocket parts.
Proposed solution:
A 3D template with evenly spaced holes that align with the desired location on the cylindrical surface

## Slide 12: Design of a deflector plate
Purpose-It redirect the intense heat and flames away from the rocket during lift off of the rocket.
N3 design Proposed design
Non uniform distribution of exhaust gases.Certain areas exposed to high heat and forces

## Slide 13: THANK
YOU