## Slide 1
SOLID PROPULSION TEAM
WEEK 12 REPORT

## Slide 2
Tasks Done
  Cooking of grains
  Repair of test stand
  Machining of nozzle and bulkheads
  Drilling and tapping M8 holes on the bulkheads
  Machining of casting rod
  Loading of grains in motor casing
  Checking ignition circuit
  Calibrating loadcell
  Static test

## Slide 3
#83 Cooking of grains
cooked 6 grains with 16.98mm port diameter and one for 25mm port diameter
preheating sorbitol
Weighing the ingredients
mixing and cookiing the mixture

## Slide 4
#83 Cooking of grains
cooked 6 grains with 16.98mm port diameter and one for 25mm port diameter
demolding and weighing
Casting in molds
Storing

## Slide 5
The parts of the test stand destroyed during the previous static test were repaired
#110 Repair of test stand

## Slide 6
  Drilled holes using 6mm diameter drill bit
  First tapped using M7 taps
  Finished tapping using M8 taps
Drilling and tapping M8 holes

## Slide 7
Turned one more grain casting rod from 25mm diameter shaft to 16.9mm d
#140 Machining of casting rod

## Slide 8
All the components and connections were good
Checking ignition circuit

## Slide 9
A known mass is used to calibrate the load cell.
Calibrating loadcell

## Slide 10
Loading of grains in motor casing
Grains with 16.98mm port diameter were loaded in the 2.5mm thick motor casing

## Slide 11
The static fire test was aimed at checking the improvement of the new grains and the strength of the 2,5mm thick motor casing
Static test
maximum thrust :407kgf
or 3992.67N

## Slide 12
  Machining of motor casing
  Machining bulkheads and nozzles
  Cooking of grains #83
  Adding buzzers and lights in the circuit
Tasks to be done next week

## Slide 13
THANK
YOU